# CPPOCL Unit Test Framework

This unit test framework is designed to be used with C++ and only requires only Test.hpp to be included.
To make it easier and faster to write the unit tests, macros have been used for defining the tests for functions, member functions or general purpose.
Tests can be written to verify correct functionality or performance.
Unit tests have been written to test this framework.
### Overview of using the macros
The test macros allow unit testing of a function, member function or a general test to be written.
It's also possible to override the names used in the macros so that the output accurately describes the function name or arguments.
Within the test macros, checker macros can be used to test various conditions for your unit tests.
These macros can be found in TestMacros.hpp.
### Overview of helper functions
The framework also provides so helper functions for doing some basic but common manipulation of basic data types, i.e. char*.
If for any reason you don't want these helper functions to be enabled, then define OCL_TEST_HELPERS_DISABLED pre-processor in your build.
These helper functions also provide support for char* and wchar_t* string pointers.
These helpers functions can be found in TestClassHelperFunctions.inl.
### Macros for testing functionality or performance
These macros are either general, specific to a C/C++ function or a C++ member function of a class.
When timing a test, the secs and millisecs represent the sample time to run the test.

TEST(name)
TEST_FUNCTION(function_name, args)
TEST_FUNCTION_TIME(function_name, args, secs, millisecs)
TEST_MEMBER_FUNCTION(class_name, function_name, args)
TEST_MEMBER_FUNCTION_TIME(class_name, function_name, args, secs, millisecs)
TEST_CONST_MEMBER_FUNCTION(class_name, function_name, args)
TEST_CONST_MEMBER_FUNCTION_TIME(class_name, function_name, args, secs, millisecs)
### Macros for checking conditions
These macros are used to perform individual checks for function calls, return types, etc.

CHECK_TRUE(expression)
CHECK_FALSE(expression)
CHECK_EQUAL(value1, value2)
CHECK_NOT_EQUAL(value1, value2)
CHECK_GREATER(value1, value2)
CHECK_GREATER_EQUAL(value1, value2)
CHECK_LESS(value1, value2)
CHECK_LESS_EQUAL(value1, value2)
CHECK_NULL(value)
CHECK_NOT_NULL(value)
CHECK_ZERO(value)
CHECK_NOT_ZERO(value)
CHECK_STRCMP(value1, value2)
CHECK_COMPARE(value1, value2)
CHECK_NOT_COMPARE(value1, value2)
CHECK_TIME(function_call)
CHECK_PERFORMANCE(function_call, min_iterations)
CHECK_EXCEPTION(expression)
CHECK_ALL_EXCEPTIONS(expression)
### Macros for customizing test
These macros provide further control over the output produced for each test

TEST_FAILURE_INDENT	/* Set number of spaces to indent error information */
TEST_OVERRIDE_FUNCTION_NAME	/* Set the function name for output, e.g. “operator=” */
TEST_OVERRIDE_ARGS	/* Set the argument names for output, e.g. “int, int” */
TEST_OVERRIDE_FUNCTION_NAME_ARGS	/* Set the function name and arguments for output */
### Helper functions
While in a unit test, these functions are provided as helpers for common functionality that might be required when working with const char* or const wchar_t* types.

StrLen	/* Return the length of a char* or wchar_t* variable as a size_t */
StrEnd	/* Return a pointer to the end of the string, i.e. position of '\0' */
SetStr	/* Set a const char* pointer and length from a source string */
StrCpy	/* Same as strcpy (without Microsoft warnings) */
StrCmp	/* Same as strcmp (without Microsoft warnings) */
CharCount	/* Count all characters matching character(s) to find in string */
MemCmp	/* Same as memcmp */
MemSet	/* Sets each element to a value */
IsDigit	/* Return true when character is in '0'..'9' */
ToInt	/* Convert character or string to integer type */
Sleep	/* Sleep in milliseconds */
### Examples for unit tests
// Only need to call this once for all unit tests, outside of any test.
TEST_FAILURE_INDENT(4);

// Perform some checks on some functions.
TEST(TestSomeFunctions)
{
    std::string str;
    CHECK_TRUE(str.empty());
    CHECK_ZERO(str.length());
}

// Test function std::min(int, int)
TEST_FUNCTION(min, ints)
{
    TEST_OVERRIDE_FUNCTION_NAME_ARGS(“std::min”, “int, int”);
    CHECK_EQUAL(min(1, 2), 1);
}

// Test member function std::string::insert(size_t, std::string)
// NOTE: NA is pre-defined to signify that function doesn't have arguments.
TEST_MEMBER_FUNCTION(string, insert, size_t_insert, NA)
{
    TEST_OVERRIDE_ARGS(“size_t, string const&”);
    std::string str("ello");
    CHECK_EQUAL(::strcmp(str.insert(0, "h").c_str(), "hello"), 0);
}

TEST_CONST_MEMBER_FUNCTION(string, length, NA)
{
    std::string str;
    CHECK_ZERO(str.length ());
}
### Examples for performance tests
// Test min for a sample time period of 1.5 seconds.
TEST_FUNCTION_TIME(min, ints, 1, 500)
{
    TEST_OVERRIDE_FUNCTION_NAME_ARGS(“std::min”, “int, int”);
    CHECK_TIME(min(1, 2));
}

// Test string::length for a sample time period of 1 second.
TEST_CONST_MEMBER_FUNCTION_TIME(string, length, 1, 0)
{
    std::string str = "Hello World!";
    CHECK_TIME(str.length());
}
### Examples of helper functions
char const* str = “Hello”;
CHECK_EQUAL(StrLen(str), 5U);

char const* end = StrEnd(str);
CHECK_EQUAL(str, end + 5);

char* str_cpy = new char[StrLen(str)+1];
CHECK_NOT_NULL(str_cpy);
StrCpy(str_cpy, str);

CHECK_EQUAL(StrCmp(str_cpy, str), 0);

CHECK_EQUAL(CharCount(str, 'e'), 1U);

CHECK_ZERO(MemCmp(str_cpy, str));

CHECK_TRUE(IsDigit('1'));

StrCpy(str_cpy, “12”);
int value = 0;
CHECK_TRUE(ToInt(str_cpy, value));
CHECK_EQUAL(value, 12);

wchar_t wstr[10];
// NOTE: MemSet works with elements and not bytes.
MemSet(wstr, 10, L'\0');